## Slide 1: HOM Dampers for the MAX IV 100 MHz RF Cavities

## Slide 2: Outline
Introduction
  Motivations
  HOM Damper Guidelines
HOM Dampers EM Design
  HOMs
  All-but-L7 HOM Dampers
  Simulation Studies
Cold RF Measurements
Final Remarks

## Slide 3: Introduction

## Slide 4: The MAX IV Accelerators
Slide by S. Werin

## Slide 5: Motivations
HOMs in the MAX IV 3 GeV ring 100 MHz cavities are the main driving force of coupled-bunch motion.
Several effective mitigating measures have been in place since several years:
  Harmonic cavities
  Feedback systems
  Cavity temperature tuning
HOM dampers will provide improved repeatability of beam conditions by removing the very driving forces of coupled bunch motion rather than counteracting their effects through feedback or increased synchrotron frequency spread.

## Slide 6: 100 MHz RF Cavity
Tuning mechanism Available ports
(b)
E-field (dB)
Beam
Deformable
endplate
Beam
Deformable
endplate
Normal H-field (dB)
Photos from: Jonas Björklund Svensson, ”Characterization of Higher Order Modes in the MAX IV Active 100 MHz Cavities”
Notes: Concept employed at MAXLAB
Capacitively loaded, deformable endplate
Fundamental coupler, HOM damper ports, LLRF ports
Fundamental mode, low E-field regions high H-field regions and axissymmetry

## Slide 7
+ Unperturbed axisymmetric simulations
Notes: Comparing R/Q
Strongest HOMs

## Slide 8: Guidelines
Damping guidelines:
  All modes but L7 damped below 3 kΩ shunt impedance
  Leave L7 undamped
Design guidelines:
  Compact
  Simple to manufacture
  Use off-the-shelf components for the complex parts
  Provide cooling solution (no welding between water and vacuum media)

## Slide 9: EM Design

## Slide 10: Axisym. E-field distributions for the HOMs
Position 1
Position 2
Pos. 3
L1
L0
Position 1
Position 2
Pos. 3
L2
Position 1
Position 2
Pos. 3
L4
Position 1
Position 2
Pos. 3
L7
Position 1
Position 2
Pos. 3
L10
Position 1
Position 2
Pos. 3
L12
Position 1
Position 2
Pos. 3
L8
Position 1
Position 2
Pos. 3

## Slide 11: L7 Degenerate Twins Example: J-probe
Long. Shunt Impedance
R|| [Ω]
Frequency [GHz]
R|| / Q [Ω]
Long. R over Q
Frequency [GHz]
*
*
*
*
Unperturbed
Goal

## Slide 12: All-but-L7 HOM Dampers (Pos. 2 and 3)
75 dB fundamental power rejection

## Slide 13: All-but-L7 Dampers: Complete Model

## Slide 14: Studies Performed
Wakefield vs. Eigenmode solvers benchmark
Sensitivity analysis
  Mechanical tolerance for cavity radius (min, max and nominal)
  Parked and Tuned (99.63 MHz and 99.93 MHz) conditions
  20 °C and 90 °C cavity temperature
Power deposition (fundamental + HOMs) and thermal simulations
Detailed model, HOMs coupling to the transmission line (next slide)

## Slide 15: Detailed Cav. Model: Line Length
coupler
stub
line
Pump station
grids
Position 1
Port
Position 2
damper
Position 3
damper
LLRF
port
Extra coupler port
158°
-40°
0°

## Slide 16: Cold RF Measurements

## Slide 17: Measurement Setup
Beam port
antenna
LLRF pick-up loop
Pos. 2 Damper
Pos. 1
Damper
Phase shifter

## Slide 18: Phase Shifter (PS) Sweep: L0 to L4
Simulation (eq. 25 °C)
Measurement (45 °C)

## Slide 19
Simulation (eq. 25 °C)
Measurement (45 °C)
Phase Shifter (PS) Sweep: L7 to L12

## Slide 20: Without vs. With HOM Dampers
L0
L1
L2
L4
L7
L8
L10
L12
TL
- Circ. TL
TL

## Slide 21: Measurements: Other Studies Performed
Parked vs Tuned (99.63 MHz and 99.93 MHz)
Temperature (25 °C and 45 °C)
U-piece
  5-12 cm
  elongation
Transmission line
with circulator
Tunnel
RF Lab

## Slide 22: Conclusion

## Slide 23: Final Remarks
We have designed and built probe-type HOM dampers for the MAX IV 100 MHz cavities
  They can damp the HOMs by large factors (10-200)
  One mode, L7, is left unaffected so it can be dealt with by temperature tuning
  The effect of the transmission line connected to the cavity is very important to define the damper performance
The prototypes will begin RF conditioning next week
The cavity with the HOM dampers is scheduled to be installed during the winter shutdown
  U-piece dimension tested on site
Limitations in the ‘with vs. without’ HOM dampers comparison
  R/Q of some modes change considerably
  Bead-pull and stretched-wire methods are too invasive (vacuum wise)
  Beam-based measurement for the final quantification

## Slide 24
Thank you!

## Slide 25: Backup Slides

## Slide 26: Mechanical and Thermal Aspects

## Slide 27: Mechanical Design: Position 2 Damper
Courtesy of
Karl Åhnberg and Mohammad
Al-Najdawi

## Slide 28: Mechanical Design: Position 3 Damper
Courtesy of
Karl Åhnberg and Mohammad
Al-Najdawi

## Slide 29: Thermal Simulation Inputs
Heat Load Considerations
  I0 = 500 mA
  No bunch roll-off in frequency
  HOM freq. shifted to the nearest rev. harmonic
  Uneven fill
Thermal Simulation BCs:
  convection to air at 24 ◦C
  and h = 5 W/m2 ·◦ C
  convection to water at 70 ◦C and
  h = 1 · 104 W/m2 · ◦C
  radiation at 25 ◦C and emissivity of 0.2
    Probe
    Inside the series stub
Considered distribution
Courtesy of Francis Cullinan

## Slide 30: MAX IV Main Cavity
*6
 | Main cavities
Type | Capacity Loaded, Normal Conducting
Frequency tuning | Elastic one-side deformation
HOM dampers | Ports available, not used (yet)
For 3 GeV ring: | 
Max voltage/cavity | 300 kV
Max wall loss/cavity | 27 kW
Max power to beam/cav | 500 kW/6 = 83 kW
Optimum coupling | 4.1
Å. Andersson
Facilities using such cavity type:
SOLARIS (Poland)
SLRI (Thailand)
ASTRID (Denmark)
ILSF (Iran)

## Slide 31: Thermal Simulation Results
Courtesy of Karl Åhnberg and Mohammad Al-Najdawi
Pfund = 35 W; PHOM = 1.6 W (pin) + 1.23 W (cer.)
L4 (82.7%), L12 (10.8%), L10 (4.8%)
Pfund = 28 W; PHOM = 0.72 W (pin) + 0.53 W (cer.)
L1 (40.9%), L10 (28.7%), L4 (17.5%)

## Slide 32: Damping Guidelines
(optimum cav. temperature for each point)
Notes: HOM model, cav 20, 500 mA

## Slide 33: Rod Probes to 50 Ω Lines
Pos. 1
Pos. 2
Pos. 3
Courtesy of David Olsson

## Slide 34: L7 Degenerate Twins Example: J-probe
Run 1
Run 5
Run 13
Run 14
1 |  | 2 |  | ← Twin # → | 1 |  | 2 | 
0 | 90 | 0 | 90 | ← Phase (o) → | 0 | 90 | 0 | 90
E-field Magnitude
Notes: Conclusion: leave L7 unattended

## Slide 35: Wakefield vs. Eigenmode Solvers Benchmark

## Slide 36: Sensitivity Analysis

## Slide 37: Extraction Circuits Ideas
D. Olsson, MAX IV
KEK
CERN
KEK

## Slide 38: All-but-L7 HOM Dampers: Endplate
Current Design
50 dB fundamental power rejection
(~95 W for 30 kW)
75 dB fundamental power rejection
(~9.5 W for 30 kW)

## Slide 39: All-but-L7 HOM Dampers: Mantel
Current Design